## Slide 1: GOES-16 Satellite Receiver
Requirements and Engineering Standards
Theodore Mathews IV, Jonathan Massner, Riley Stuart, Jordan Tillotson, Nicholas Butts, Yong Lim
Notes: Hello and welcome to our senior design project requirements and engineering standards overview. The overall goal of our project is to build a satellite receiver that will receive image products from the Geostationary Operational Environmental Satellite - 16, also referred to as the GOES-16. This weather satellite is in geostationary orbit. We will begin by discussing the functional requirements for the project.

## Slide 2: Requirements - Functional
Antenna: The antenna for this receiver will be a Wifi grid antenna with a design frequency of 2.4 GHz
  Size Requirement: 1.1 m in diameter
  Frequency: 1694.1 MHz. The antenna is designed for wifi, the feedhorn must be modified for this frequency.
  Connector: N or SMA
  Polarization: Linear, vertical orientation
  Aiming: ± 2° in both rotation and elevation to ensure maximum gain
Filtering & Amplification: Following the Antenna, the signal needs to be filtered and amplified.
  Gain: > 20 dB
  Bandwidth: >1.205 MHz and <10 MHz. Recent spectrum auctions now allow cell phone use on similar bands.
Notes: The antenna for this project is a balance between physical size and cost. NOAA suggests a dish size of at least 1 meter for reliable reception and there have been projects published on NOAA’s website that make use of wifi dish antennas which happen to be just over 1 meter in diameter.
The dishes feed horn has to be modified to work at the 1.69 GHz frequency that we care about. The mounting system for the antenna needs to be both precise enough to aim within 2 degrees in both rotation and elevation and sturdy enough to keep the antenna pointed correctly as reception for a single image can take over 15 minutes.
Due to the low signal levels of the received signal, we will apply band filtering immediately after the antenna, followed by a low noise amplifier, and then a narrow band filter to ensure we only obtain the signal that we care about.

## Slide 3: Requirements - Functional
Downconverter: Downmix the received HRIT signal for digitization
  Frequency: 1694.1 MHz
  Bandwidth: > 1.205 MHz
Digitizer: Digitizes the IF from the downconverter
  Sample Rate: > 2.5 Msps at the IF frequency
Software: Decodes and processes the HRIT/EMWIN data from the received signal
  Ability to successfully decode the received signal and produce weather product output (images).
Notes: Once we have the filtered and amplified signal from the antenna we need to down convert the frequency from the received 1.69 GHz to something that can be easily digitized. The exact IF frequency and down conversion architecture is still under consideration and review.
Regardless of the final IF frequency, we need to be able to sample at least 1.205 MHz of spectrum thus we will need a sample rate greater than about 2.5 mega samples per second at our IF frequency.
The software needs to take the sampled signal, decode it, packetize it, and extract the images from the transmission.

## Slide 4: Requirements - Environmental
Line of Sight:
  The antenna needs a clear line of sight to the satellite, limiting possible setup locations.
Semi-Portable:
  Unable to permanently mount the antenna on campus due to cost and planning requirements
  Long reception times complicate testing
Clouds & Weather:
  Cloud cover should not impact reception.
  Equipment will need to be weather resistant if a permanent installation is desired.
Notes: The environmental requirements for our project include the physical location of the antenna, a clear view of the sky, and the weather. Due to the costs associated with mounting anything to ISU owned buildings, the antenna will need to be easily setup and taken down. At the same time, any testing or reception of images requires extended periods of time with the antenna setup in a fixed location.
Cloud cover and rain should not negatively impact reception, but all of the equipment will need to be weather resistant for extended outdoor usage.

## Slide 5: Requirements - Economic
Budget:
  ~ $1,000
Components:
  Use COTS (Commercial off-the-shelf) where possible for larger components (antenna, preamps, computers).
  RF and Digitization section are the primary hardware design focus.
Notes: The project has a budget of $1000. We must stay within this budget for all of our research, prototyping, and final design costs. We plan to use commercial, off-the-shelf components where possible for the larger parts of the project. The RF and Digitization section is the primary hardware design focus of this project.

## Slide 6: Engineering Standards - Documentation
Circuits:
  Schematics
  Parts lists
  Simulation results
Digital Design:
  High and low level schematics
  Simulation results
Software:
  Source code
  In-line comments
  External documentation
  Consistent and organized file structure
Notes: The engineering standards used for this project will be consistent with the current industry standards. We plan on incorporating many CAD tools that are used by engineers in the professional world. We will be using PSPICE, along with prototyping and testing to validate our circuit designs. Schematics will be included for all hardware designs.
We will also use efficient coding methodologies in all of our software and FPGAs. The software will make use of existing software libraries when practical, documented, and organized to allow engineers outside of the project to be able to understand our system.